## Slide 1: SCHISM 2D setup
Joseph Zhang

## Slide 2: Some UNIX commands
Create dir: mkdir
Go to a dir: cd
Copying/moving
  Local system: cp, mv, rsync
  Across systems: rsync, scp
File editing: vi, nano, …

## Slide 3: SCHISM compilation
git cmd from online manual to download the version-controlled source code
git checkout tags/v5.11.1 (inside the schism/ you cloned)
cmake (on kuro)
  cp ~yinglong/.cshrc.kuro ~/ (to get my env on kuro)
  mkdir build (inside the schism/ you cloned)
  cd build
  cmake -C ../cmake/SCHISM.local.build -C ../cmake/SCHISM.local.kuro ../src/ (can be copied from inside ../cmake/README)
  make –j8 pschism

## Slide 4
Job scheduler
Batch scripts
  Sciclone uses Torque (PBS) or slurm to schedule and manage jobs
Submission
  Submitting jobs from head node to compute nodes
  qsub <batch script> (for PBS)
  sbatch <batch script> (for slurm)
  System messages may be found in <job name>.[eo]<job id> or standard output specified in script (err2.out below)
  Can launch parallel or serial jobs
Job control
  PBS: qstat –u <uid>, qdel <job id>
  SLURM: squeue –u <uid>, scancel <job id>

## Slide 5
Batch script
PBS (run_bora)
#!/bin/tcsh
#SBATCH --job-name=25b
#SBATCH --nodes=10 --ntasks-per-node=32
#SBATCH --constraint=femto
##Do not allow sharing of nodes
#SBATCH --exclusive
###Max walltime is 72 hrs
#SBATCH -t 60:00:00
##SBATCH --mail-type=all
srun ./pschism_FEMTO_TVD-VL 6 >& err2.out
#!/bin/tcsh
#PBS -N 01b
#PBS -l nodes=20:bora:ppn=20
#PBS -l walltime=40:00:00
##PBS -M yjzhang@vims.edu
##PBS -m be
cd $PBS_O_WORKDIR
#Pure MPI
mvp2run -v -C 0.05 ./pschism_BORA_TVD-VL 6 >& err2.out
SLURM (run_femto)
Exercise: cp a test case to your own data10/ and launch it on kuro
/sciclone/home/yinglong/DISKS/schism10/schism_verification_tests.2/Test_QuarterAnnulus

## Slide 6: SCHISM 2D Primer
Online manual and wiki resource: www.schism.wiki
  Version hopping: consult beta_notes and sample files in each source code bundle to keep track of changes
  Let’s stick to tag v5.11.1 (and online manual)
Pre- and post-processing scripts (in python, matlab, FORTRAN etc)
Bare minimum (for pre-processor)
  Generate a hgrid.gr3 with simplest possible b.c. (e.g., no open boundary)
  Run SCHISM in 2D config: manning.gr3, param.nml, bctides.in, vgrid.in (2 levels)
  Pre-processing with ipre=1 first to catch mesh and other issues
Then proceed to more complex set-ups
  Establish a good workflow and be willing to revise the mesh

## Slide 7: Sample run directory
/sciclone/home10/yinglong/vims20/schism_verification_tests/Test_CORIE/% ls -L *.gr3 *.ll *.ic
albedo.gr3 diffmax.gr3 drag.gr3 hgrid.gr3 SAL_nudge.gr3 TEM_nudge.gr3 windrot_geo2proj.gr3
diffmin.gr3 estuary.gr3 hgrid.ll watertype.gr3
/sciclone/home10/yinglong/vims20/schism_verification_tests/Test_CORIE/% ls -L *.in *.nml
bctides.in vgrid.in param.nml
/sciclone/home10/yinglong/vims20/schism_verification_tests/Test_CORIE/% ls -L *.th*
flux.th TEM_1.th <- ASCII
/sciclone/home10/yinglong/vims20/schism_verification_tests/Test_CORIE/% ls -L *.nc
hotstart.nc SAL_nu.nc TEM_nu.nc
/sciclone/home10/yinglong/vims20/schism_verification_tests/Test_CORIE/% ls -L
albedo.gr3 drag.gr3 hotstart.nc postpros.pl watertype.gr3 bctides.in
windrot_geo2proj.gr3 estuary.gr3 SAL_nudge.gr3 TEM_1.th
diffmax.gr3 hgrid.gr3 outputs/ SAL_nu.nc TEM_nudge.gr3 tvd.prop
diffmin.gr3 flux.th hgrid.ll param.nml sflux/ TEM_nu.nc vgrid.in

## Slide 8: Outputs

## Slide 9: Sample output directory
/sciclone/home10/yinglong/vims20/schism_verification_tests/Test_CORIE/% ls outputs/
global_to_local.prop hotstart_000010_960.nc hotstart_000077_960.nc local_to_global_000023 local_to_global_000090 nonfatal_000035 nonfatal_000102 salinity_2.nc zCoordinates_10.nc
horizontalVelX_10.nc hotstart_000011_960.nc hotstart_000078_960.nc local_to_global_000024 local_to_global_000091 nonfatal_000036 nonfatal_000103 salinity_3.nc zCoordinates_11.nc
horizontalVelX_11.nc hotstart_000012_960.nc hotstart_000079_960.nc local_to_global_000025 local_to_global_000092 nonfatal_000037 nonfatal_000104 salinity_4.nc zCoordinates_12.nc
horizontalVelX_12.nc hotstart_000013_960.nc hotstart_000080_960.nc local_to_global_000026 local_to_global_000093 nonfatal_000038 nonfatal_000105 salinity_5.nc zCoordinates_13.nc
horizontalVelX_13.nc hotstart_000014_960.nc hotstart_000081_960.nc local_to_global_000027 local_to_global_000094 nonfatal_000039 nonfatal_000106 salinity_6.nc zCoordinates_14.nc
horizontalVelX_14.nc hotstart_000015_960.nc hotstart_000082_960.nc local_to_global_000028 local_to_global_000095 nonfatal_000040 nonfatal_000107 salinity_7.nc zCoordinates_15.nc
horizontalVelX_15.nc hotstart_000016_960.nc hotstart_000083_960.nc local_to_global_000029 local_to_global_000096 nonfatal_000041 nonfatal_000108 salinity_8.nc
Using new I/O, the output dir looks like this:
There are two I/O modes inside SCHISM
  OLDIO: outputs results per MPI rank
  New I/O: scribed based for global nc outputs (no need to combine), except for hotstart and max outputs
  Station time series outputs are also combined for you

## Slide 10: Pre- and post-combined outputs
hotstart_it=960.nc
hotstart_000001_960.nc
hotstart_000399_960.nc
…………………..
combine_hotstart7.f90
hotstart_000000_960.nc
(combined output)
Netcdf outputs
maxelev_000000 maxelev_000001 …………… maxelev_000399
ASCII
maxelev.gr3
combine_gr3.f90
(max elevation over all time steps)

## Slide 11: New I/O
/sciclone/home/yinglong/DISKS/schism10/BlackSea/RUN24h/outputs% ls *_1.nc
horizontalVelX_1.nc horizontalVelY_1.nc out2d_1.nc salinity_1.nc temperature_1.nc verticalVelocity_1.nc zCoordinates_1.nc
All 2D outputs are in out2d*.nc
Each 3D variable has its own output; vector (horizontal velocity) outputs have x,y components in separate files
# of scribes = (# of 3D variables) + 2
  Vector output count as 2
  Code will run if you specify more scribes than necessary

## Slide 12: Main diagnostic output (mirror.out, by rank 0)
Run begins at 20171026, 082037.556
You are using baroclinic model
# of tracers in each module: 1 1 0 0
0 0 0 0 0 0
0
Total # of tracers= 2
Index ranges of each module: 1 1 2 2
3 2 3 2 3 2
3 2 3 2 3 2
3 2 3 2 3 2
# of global outputs= 29
done reading param.in; s2_mxnbt in param.in = 3.00000000000000
lhas_quad= F
mnei, mnei_p = 10 11
lhas_quad= F
Global Grid Size (ne,np,ns,nvrt): 38960 20641 59615 54
**********Augmented Subdomain Sizes**********
rank nea ne neg nea2 neg2 npa np npg npa2 npg2 nsa ns nsg nsa2 nsg2
0 1071 821 250 1071 0 634 521 113 634 0 1701 1345 356 1701 0
1 1055 828 227 1055 0 611 514 97 611 0 1664 1349 315 1664 0
2 981 794 187 981 0 588 500 88 588 0 1566 1293 273 1566 0
…………………….
heat budge model completes...
time stepping begins... 1 26880
heat budge model completes...
done adjusting wind stress ...
done flow b.c.
done MYG-UB...
done hvis...
done backtracking
done 1st preparation
done 2nd preparation
done solver; etatot= 0.939833361180156 ; average |eta|= 4.553235604767967E-005
done solving momentum eq...
done solving w
done tracer transport...
done solving transport equation
done recomputing levels...
done density and flux calculation...
TIME STEP= 1; TIME= 90.000000
heat budge model completes...
done adjusting wind stress ...
done flow b.c.
Quick check on the health of a run can be done using averaged |eta|
Check if it’s unreasonable (or NaN)

## Slide 13: Sample netcdf output file: new IO
netcdf out2d_2 {
dimensions:
nSCHISM_hgrid_node = 20641 ;
nSCHISM_hgrid_face = 38960 ;
nSCHISM_hgrid_edge = 59615 ;
nMaxSCHISM_hgrid_face_nodes = 4 ;
nSCHISM_vgrid_layers = 54 ;
one = 1 ;
two = 2 ;
time = UNLIMITED ; // (96 currently)
variables:
double time(time) ;
time:i23d = 0 ;
time:base_date = " 2002 4 30 0.00 8.00" ;
time:units = "seconds since 2002-04-30T00:00:00+08" ;
time:standard_name = "time" ;
time:axis = "T" ;
double minimum_depth(one) ;
minimum_depth:units = "m" ;
char SCHISM_hgrid(one) ;
SCHISM_hgrid:long_name = "Topology data of 2d unstructured mesh" ;
SCHISM_hgrid:topology_dimension = 2 ;
double SCHISM_hgrid_node_x(nSCHISM_hgrid_node) ;
SCHISM_hgrid_node_x:axis = "X" ;
SCHISM_hgrid_node_x:location = "node" ;
double SCHISM_hgrid_node_y(nSCHISM_hgrid_node) ;
SCHISM_hgrid_node_y:axis = "Y" ;
int SCHISM_hgrid_face_nodes(nSCHISM_hgrid_face, nMaxSCHISM_hgrid_face_nodes) ;
SCHISM_hgrid_face_nodes:start_index = 1 ;
SCHISM_hgrid_face_nodes:_FillValue = -1 ;
SCHISM_hgrid_face_nodes:cf_role = "face_node_connectivity" ;
int SCHISM_hgrid_edge_nodes(nSCHISM_hgrid_edge, two) ;
SCHISM_hgrid_edge_nodes:start_index = 1 ;
SCHISM_hgrid_edge_nodes:_FillValue = -1 ;
SCHISM_hgrid_edge_nodes:cf_role = "edge_node_connectivity" ;
float dryFlagNode(time, nSCHISM_hgrid_node) ;
dryFlagNode:i23d = 1 ;
dryFlagNode:coordinates = "SCHISM_hgrid_node_x SCHISM_hgrid_node_y" ;
dryFlagNode:location = "node" ;
dryFlagNode:grid_mapping = "crs" ;
dryFlagNode:mesh = "SCHISM_hgrid" ;
float elevation(time, nSCHISM_hgrid_node) ;
elevation:i23d = 1 ;
elevation:coordinates = "SCHISM_hgrid_node_x SCHISM_hgrid_node_y" ;
connectivity
Most static info is found in out2d_*.nc
Use ncdump to view file
See: /sciclone/home/yinglong/DISKS/schism10/schism_verification_tests.2/Test_CORIE

## Slide 14: Sample netcdf output file for 3D variables
netcdf salinity_2 {
dimensions:
nSCHISM_hgrid_node = 20641 ;
nSCHISM_hgrid_face = 38960 ;
nSCHISM_hgrid_edge = 59615 ;
nMaxSCHISM_hgrid_face_nodes = 4 ;
nSCHISM_vgrid_layers = 54 ;
one = 1 ;
two = 2 ;
time = UNLIMITED ; // (96 currently)
variables:
double time(time) ;
time:i23d = 0 ;
time:base_date = " 2002 4 30 0.00 8.00" ;
time:units = "seconds since 2002-04-30T00:00:00+08" ;
time:standard_name = "time" ;
time:axis = "T" ;
float salinity(time, nSCHISM_hgrid_node, nSCHISM_vgrid_layers) ;
salinity:i23d = 2 ;
salinity:missing_value = 9.96921e+36f ;
salinity:coordinates = "SCHISM_hgrid_node_x SCHISM_hgrid_node_y" ;
salinity:location = "node" ;
salinity:grid_mapping = "crs" ;
salinity:mesh = "SCHISM_hgrid" ;
data:
Other netcdf outputs (3D) only contain a few variables
visIT and other tools understand this division of source info

## Slide 15: Details of 2D model inputs
For an example setup, see:
~yinglong/DISKS/schism10/schism_verification_tests.2/Test_QuarterAnnulus

## Slide 16: .gr3 and .ll files
Your comments
44343 24025
1 -90.4293 30.1689 0.30
2 -90.4313 30.1625 0.30
3 -90.4327 30.1559 0.20
4 -90.4320 30.1498 0.20
………………………………………
1 3 1 2 3
2 3 2 4 5
3 4 15943 16197 15942 1401
………………………………………
nodes
elements
Boundary info
(hgrid.gr3 only)
2 = Number of open boundaries
69 = Total number of open boundary nodes
4 = Number of nodes for open boundary 1
1
2
3
4
………………………………………
12 = number of land boundaries
1756 = Total number of land boundary nodes
737 0 = Number of nodes for land boundary 1
29368
29421
29420
29467
………………………………………
Complete x,y,z info needed for hgrid.gr3 and hgrid.ll only
For other .gr3, only ‘depth’ (z) info is needed
*.gr3 essentially flips the parts in .2dm

## Slide 17: vgrid.in: 2D
2 !ivcor
2 1 1.e6 !nvrt, kz (# of Z-levels); h_s (transition depth between S and Z)
Z levels
1 -1.e6
S levels
40. 1. 1.e-4 !h_c, theta_b, theta_f
1 -1.
2 0.
Simplest way is to use a SZ format:
* You can simply copy from:
~yinglong/DISKS/schism10/schism_verification_tests.2/Test_QuarterAnnulus/vgrid.in
* Make sure to use a large enough value to account for drying (model will crash if the surface elevation falls below -40m)

## Slide 18: param.nml
FORTRAN namelist format to specify parameters
Format rules:
  Lines beginning with “!" are comments; blank lines are ignored;
  One line for each parameter in the format: keywords= value;
keywords are case insensitive; spaces allowed between keywords and "=" and
value; comments starting with “!" allowed after value;
  Value can be an integer, float/double, or string or arrays; for float/double, any of the format is acceptable: 40 40. 4.e1; use of decimal point for integers is discouraged
  Order of parameters not important
  Repeated entries: last one wins! (do not do this)
Three major sections
  CORE: mandatory parameters. If not specified, the code will crash
  OPT: optional parameters with code defaults (often a good starting point)
  SCHOUT: optional parameters that control outputs
See a sample in your own downloaded soruce code dir: schism/sample_inputs/param.nml

## Slide 19: param.nml: CORE
&CORE
!+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
! Core (mandatory) parameters; no defaults
!+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
! Pre-processing option. Useful for checking grid errors etc. Can only use 1 CPU if ipre=1
ipre = 0 !Pre-processor flag (1: on; 0: off)
! Baroclinic/barotropic option. If ibc=0 (baroclinic model), ibtp is not used.
ibc = 1 !b-tropic
ibtp = 0 !exclude transport
rnday = 30 !total run time in days
dt = 100. !Time step in sec
! Grid for WWM (USE_WWM)
msc2 = 24 !same as msc in .nml ... for consitency check between SCHISM and WWM
mdc2 = 30 !same as mdc in .nml
! Define # of tracers in tracer modules (if enabled)
ntracer_gen = 2 !user defined module (USE_GEN)
ntracer_age = 4 !age calculation (USE_AGE). Must be =2*N where N is # of age tracers
sed_class = 5 !SED3D (USE_SED)
eco_class = 27 !EcoSim (USE_ECO): must be between [25,60]
! Global output controls
nspool = 36 !output step spool
ihfskip = 864 !stack spool; every ihfskip steps will be put into 1_*, 2_*, etc...
/
* ihfskip must be multiple of nspool
For modules

## Slide 20: OPT section
* You can use lon/lat even for high-resolution inundation study!
&OPT
!-----------------------------------------------------------------------
! Coordinate option: 1: Cartesian; 2: lon/lat (hgrid.gr3=hgrid.ll in this case,
! and orientation of triangles is outward of earth)
!-----------------------------------------------------------------------
ics = 1 !Coordinate option
cpp_lon = -124 !CPP projection centers: lon; not used if ics=2
cpp_lat = 46.25 !CPP projection centers: lat
!-----------------------------------------------------------------------
! Hotstart option. 0: cold start; 1: hotstart with time reset to 0; 2:
! continue from the step in hotstart.in
!-----------------------------------------------------------------------
ihot = 0
!-----------------------------------------------------------------------
! Hydraulic model option. If ihydraulics/=0, hydraulics.in
! is required. This option cannot be used with non-hydrostatic model.
!-----------------------------------------------------------------------
ihydraulics = 0

## Slide 21: OPT section: ihot
t=0
Dt
ihot=0 (cold start)
Most parts of the code do not use the calendar time
  Exceptions: air-sea exchange, WWM etc
The code basically starts from t=0 and marches thru time with Dt
2*Dt
3*Dt
t=0
t1
ihot=2 (restart from hotstart.nc)
‘Hindcast’ mode
ihot=1 (reset t=0 and start from hotstart.nc)
t=0 (t1)
t=0
Original cold start
‘Forecast’ mode

## Slide 22: Hotstart procedure
ihot=2: no need to change any inputs (because the time origin is the same); simply set ihot=2 in param.nml, combine hotstart outputs (hotstart_00*.nc) into hotstart.nc, and go
ihot=1: need to change most time history inputs (exception: sflux) to re-align time origin

## Slide 23: OPT: control of dissipation in momentum
indvel=0, ishapiro=1, ihorcon=0, shapiro0=0.5 for most barotropic applications
!-----------------------------------------------------------------------
! Methods for computing velocity at nodes.
! If indvel=0, conformal linear shape function is used; if indvel=1, averaging method is used.
! For indvel=0, a stabilization method is needed (see below).
!-----------------------------------------------------------------------
indvel = 0
!-----------------------------------------------------------------------
! 2 stabilization methods, mostly for indvel=0.
! (1) Horizontal viscosity option. ihorcon=0: no viscosity is used; =1: Lapacian;
! =2: bi-harmonic. If ihorcon=1, horizontal viscosity _coefficient_ (<=1/8, related
! to diffusion number) is given in hvis_coef0, and the diffusion #
! is problem dependent; [0.001-1/8] seems to work well.
! If ihorcon=2, diffusion number is given by hvis_coef0 (<=0.025).
! If indvel=1, no horizontal viscosity is needed.
! (2) Shapiro filter (see below)
!
! For non-eddying regime applications (nearshore, estuary, river), easiest option is:
! indvel=0, ishapiro=1 (shapiro=0.5), ihorcon=inter_mom=0
! For applications that include eddying regime, refer to the manual.
!-----------------------------------------------------------------------
ihorcon = 0
hvis_coef0 = 0.025 !const. diffusion # if ihorcon/=0; <=0.025 for ihorcon=2, <=0.125 for ihorcon=1
! cdh = 0.01 !needed only if ihorcon/=0; land friction coefficient - not active yet
!-----------------------------------------------------------------------
! 2nd stabilization method via Shapiro filter. This should normally be used
! if indvel=ihorcon=0. To transition between eddying/non-eddying regimes, use
! indvel=0, ihorcon/=0, and ishapiro=-1 (shapiro.gr3).
!-----------------------------------------------------------------------
ishapiro = 1 !on/off flag
shapiro = 0.5 !Shapiro filter strength, needed only if ishapiro=1; max is 0.5
!-----------------------------------------------------------------------
! Horizontal diffusivity option. if ihdif=1, horizontal diffusivity is given in hdif.gr3
!-----------------------------------------------------------------------
ihdif = 0

## Slide 24: OPT
!-----------------------------------------------------------------------
! Bottom friction.
! nchi=0: drag coefficients specified in drag.gr3; nchi=-1: Manning's
! formulation (even for 3D prisms) with n specified in manning.gr3.
! nchi=1: bottom roughness (in meters) specified in rough.gr3 (and in this case, negative
! or 0 depths in rough.gr3 indicate time-independent Cd, not roughness!).
! Cd is calculated using the log law, when dzb>=dzb_min; when dzb<dzb_min,
! Cd=Cdmax, where Cdmax=Cd(dzb=dzb_min).
! If iwbl/=0, nchi must =1.
!-----------------------------------------------------------------------
nchi = -1
!dzb_min = 0.5 !needed if nchi=1; min. bottom boundary layer thickness [m].
hmin_man = 1. !needed if nchi=-1: min. depth in Manning's formulation [m]
!-----------------------------------------------------------------------
! Coriolis. If ncor=-1, specify "latitude" (in degrees); if ncor=0,
! specify Coriolis parameter in "coriolis"; if ncor=1, model uses
! lat/lon in hgrid.ll for beta-plane approximation if ics=1, and in this case,
! the latitude specified in CPP projection ('cpp_lat') is used. If ncor=1 and ics=2,
! Coriolis is calculated from local latitude, and 'cpp_lat' is not used.
!-----------------------------------------------------------------------
ncor = 1 !must be 1 if ics=2
!latitude = 46 !if ncor=-1
!coriolis = 1.e-4 !if ncor=0
* manning.gr3: start with 0.025

## Slide 25: OPT
!-----------------------------------------------------------------------
! Implicitness factor (0.5<thetai<=1).
!-----------------------------------------------------------------------
thetai = 1
!-----------------------------------------------------------------------
! Point sources/sinks option (0: no; 1: ASCII inputs; -1: netcdf).
! If =1, needs source_sink.in (list of elements),
! vsource,th, vsink.th, and msource.th (the source/sink values must be single precision).
! If =-1, all info is in source.nc
! and each type of volume/mass source/sink can have its own time step and
! # of records.
! Source/sinks can be specified at an elem more
! than once, and the code will accumulate the volumes; for mass conc,
! values are applied at _net_ source elem (no summation for conc).
!-----------------------------------------------------------------------
if_source = 0
q
* thetai=1 maximizes stability (especially for severe inundation), while thetai=0.5001 maximizes accuracy. For boundary-value problems, the difference is often minor

## Slide 26: OPT: Atmospheric forcing
!-----------------------------------------------------------------------
! Atmos. option. If nws=0, no atmos. forcing is applied. If nws=1, atmos.
! variables are read in from wind.th. If nws=2, atmos. variables are
! read in from sflux_ files.
! If nws=4, ascii format is used for wind and atmos. pressure at each node (see source code).
! If nws>0, 'iwindoff' can be used to scale wind speed (with windfactor.gr3).
!
! Stress calculation:
! If nws=1 or >=4, or nws=2 and ihconsv=0, or nws=2 and iwind_form=-1,
! the stress is calculated from Pond & Pichard formulation
! If nws=2, ihconsv=1 and iwind_form=0, the stress is calculated from heat exchange
! routine;
! If WWM is enabled and icou_elfe_wwm>0 and iwind_form=-2, stress is calculated by WWM;
! otherwise the formulations above are used.
!-----------------------------------------------------------------------
nws = 2
wtiminc = 150. !time step for atmos. forcing
nrampwind = 1 !ramp-up option for atmos. forcing
drampwind = 2. !needed if nrampwind/=0; ramp-up period in days
iwindoff = 0 !needed only if nws/=0; '1': needs windfactor.gr3
iwind_form = -1
!-----------------------------------------------------------------------
! Heat and salt exchange. isconsv=1 needs ihconsv=1; ihconsv=1 needs nws=2.
! If isconsv=1, need to compile with precip/evap module turned on.
!-----------------------------------------------------------------------
ihconsv = 0 !heat exchange option
isconsv = 0 !evaporation/precipitation model
nws=2 is recommended. There are several scripts to help you prepare sflux/
pySCHISM can prepare sflux for you from GFS, HRRR, ERA5 etc
For b-tropic cases, only sflux_air* are used, which contain info: wind speed, air pressure, specific humidity, air temperature and associated atmos model grid (lon/lat)

## Slide 27: SCHOUT
!-----------------------------------------------------------------------
!Non-node centered outputs
!-----------------------------------------------------------------------
iof_hydro(27) = 0 !horizontal vel vector defined @side [m/s] {hvel_side}
iof_hydro(28) = 0 !vertical vel. @elem [m/s] {wvel_elem}
iof_hydro(29) = 0 !T @prism centers [C] {temp_elem}
iof_hydro(30) = 0 !S @prism centers [PSU] {salt_elem}
iof_hydro(31) = 0 !Barotropic pressure gradient force vector (m.s-2) @side centers {pressure_gradient}
&SCHOUT
!-----------------------------------------------------------------------
!Option for hotstart outputs (use combine_hotstart7.f90 to combine)
!-----------------------------------------------------------------------
nhot = 1 !1: output *_hotstart every 'hotout_write' steps
nhot_write = 4032 !divisible by ihfskip
!-----------------------------------------------------------------------
!Global output options (node centered)
!-----------------------------------------------------------------------
iof_hydro(1) = 1 !0: off; 1: on - elev. [m] {elevation} 2D
iof_hydro(2) = 1 !air pressure [Pa] {airPressure} 2D
iof_hydro(3) = 0 !air temperature [C] {airTemperature} 2D
iof_hydro(4) = 0 !Specific humidity [-] {specificHumidity} 2D
iof_hydro(5) = 0 !Net downward solar (shortwave) radiation after albedo [W/m/m] {solarRadiation} 2D
iof_hydro(6) = 0 !sensible flux (positive upward) [W/m/m] {sensibleHeat} 2D
iof_hydro(7) = 0 !latent heat flux (positive upward) [W/m/m] {latentHeat} 2D
iof_hydro(8) = 0 !upward longwave radiation (positive upward) [W/m/m] {upwardLongwave} 2D
iof_hydro(9) = 0 !downward longwave radiation (positive downward) [W/m/m] {downwardLongwave} 2D
iof_hydro(10) = 0 !total flux=-flsu-fllu-(radu-radd) [W/m/m] {totalHeat} 2D
iof_hydro(11) = 0 !evaporation rate [kg/m/m/s] {evaporationRate} 2D
iof_hydro(12) = 0 !precipitation rate [kg/m/m/s] {precipitationRate} 2D
iof_hydro(13) = 0 !Bottom stress vector [kg/m/s^2(Pa)] {bottomStressX,Y} 2D vector
iof_hydro(14) = 0 !wind velocity vector [m/s] {windSpeedX,Y} 2D vector
iof_hydro(15) = 0 !wind stress vector [m^2/s/s] {windStressX,Y} 2D vector
iof_hydro(16) = 0 !depth-averaged vel vector [m/s] {depthAverageVelX,Y} 2D vector
iof_hydro(17) = 0 !vertical velocity [m/s] {verticalVelocity} 3D
iof_hydro(18) = 1 !water temperature [C] {temperature} 3D
iof_hydro(19) = 0 !water salinity [PSU] {salinity} 3D
iof_hydro(20) = 0 !water density [kg/m^3] {waterDensity} 3D
iof_hydro(21) = 0 !vertical eddy diffusivity [m^2/s] {diffusivity} 3D
iof_hydro(22) = 0 !vertical eddy viscosity [m^2/s] {viscosity} 3D
iof_hydro(23) = 0 !turbulent kinetic energy {turbulentKineticEner} 3D
iof_hydro(24) = 0 !turbulent mixing length [m] {mixingLength} 3D
! iof_hydro(25) = 1 !z-coord {zCoordinates} 3D - this flag should be on for visIT etc
iof_hydro(26) = 1 !horizontal vel vector [m/s] {horizontalVelX,Y} 3D vector
Question: how many scribes should you use for this run?

## Slide 28: SCHOUT
!-----------------------------------------------------------------------
!Station output option. If iout_sta/=0, need output skip (nspool_sta) and
!a station.in. If ics=2, the cordinates in station.in must be in lon., lat,
!and z (measured from datum; not used for 2D variables).
!-----------------------------------------------------------------------
iout_sta = 0
nspool_sta = 10 !needed if iout_sta/=0
!-----------------------------------------------------------------------
! Flag for harmonic analysis for elevation. If used , need to turn on USE_HA
! in Makefile, and input harm.in. Otherwise set it to 0. Hotstart ihot=2 is not working with HA
! Outputs are harme_* and use combine_outHA to combine.
!-----------------------------------------------------------------------
iharind = 0

## Slide 29: Most important parameters are…
Momentum dissipation: indvel, ihorcon, ishapiro
  Appropriate combination of these can be used for different applications (dispersion vs diffusion)
  Should start with: indvel= ihorcon=0, ishapiro=1 (‘MB-LI’ scheme)
  If dissipation is still too high, use ishapiro=0, ihorcon=2, hvis_coef0=0.025 (or smaller). You can also use ishapiro=-1 and set the filter strength in shapiro.gr3 (or use Smagorinsky type viscosity ishapiro=2) to further tweak the dissipation
dt: appropriate time step
  Another way to control dispersion/diffusion
  Reducing dt will increase diffusion and decrease dispersion, but beware inverse CFL criterion
  Start with dt=150s
nws: use ‘2’ as much as possible
h0: minimum depth for wet/dry; may need to reduce it from 1cm to 0.1mm for compound flood studies

## Slide 30: bctides.in: a simple example
!Any comments on this line
0 40. ntip
0 nbfr
0 nope*
*Note that there is no open boundary here. This is convenient for ipre=1 (SCHISM’s pre-processor)
*If you have already created open bnd segments, use simplest b.c. (constant)

## Slide 31: SCHISM pre-processor: ipre=1
Easiest way to catch mesh errors!
Do this when you have a new mesh
Bare minimum for pre-processing (ipre=1)
  hgrid.gr3: no need to have correct bathymetry & boundaries yet (e.g., set 2 linked land bnd segments only)
  vgrid.in (1 layer for 2D for simplicity, e.g. from quarter annulus test)
  param.nml: use simplest b-tropic options (so as to not trigger other inputs)
  bctides.in: simplest
  drag.gr3/rough.gr3/manning.gr3 (to specify bottom friction, depending on the nchi specified in param.nml): use a constant (e.g. 0.025)
Pre-processing
  Prepare the mandatory input files, and set ipre=1 in param.nml
  Run SCHISM with 1 CPU only for compute (plus scribe processes)
  Check fatal.error and system outputs for fatal errors (e.g. mesh issues)
  If successful, you’d see ‘Pre-processing completed successfully!’ in your system outputs
    Under new I/O, the run may hang; simply kill the job
  If error occurs, you’ll see them in outputs/fatal.error or system outputs
  Rectify mesh/inputs errors and repeat until pre-processing is successful
Notes: Demo: /sciclone/home/yinglong/DISKS/schism10/NOAA-SECOFS/HyungJu/RUN04a_JZ/pre-proc

## Slide 32: SCHISM’s pre-processor
Exercise: your DE Bay mesh. You’ll only need:
hgrid.gr3: can use simplified open bnd config or even no open bnd
manning.gr3: constant value of 0.025
Copy from quarter annulus and edit as appropriate:
  param.nml: simplest b-tropic options
  bctides.in: simplest without tides
  vgrid.in (2 levels)

## Slide 33: bctides.in: more complex cases
12/01/2013 00:00:00 GMT
0 50. ntip
0 nbfr
2 nope
1190 2 0 0 0 Pacific
0.5 !elev B.C.
139 0 2 0 0 River
-10000. !river discharge in m3/s
A simpler example
B.C. parts specify types of B.C. imposed on each open segment
  Some flag types (‘2’) require inputs in bctides.in immediately after the flags
  Other types require separate input files (*.th* etc)
bctides.in is the most error prone input in SCHISM
Use bi-section method to ID the cause for crash
B.C. part
04/15/2004 00:00:00 PST
0 40. ntip
2 nbfr
Z0
0. 1. 0.
O1
6.759775e-05 1.15343 118.92151
4 nope
3 3 1 0 0 Georgia
Z0
0.1299680 0.000000E+00
0.1299680 0.000000E+00
0.1299680 0.000000E+00
O1
0.361010246 281.862898
0.36065857 281.918305
0.360767938 281.968364
88 3 0 0 0 ocean
Z0
8.892417E-02 0.000000E+00
8.631096E-02 0.000000E+00
........................
O1
.........................
Phases don’t matter for Z0
A more complex example
B.C. part

## Slide 34: Lateral b.c. and nudging
Variable | Type 1 (*.th) | Type 2: | Type 3 | Type 4 (*[23]D.th) | Type 5 | Type -1 | Type -4, -5 (uv3D.th); nudging | Nudging/sponge layer near boundary
h | elev.th: Time history; uniform along segment | Constant elev | Tidal amp/phases | elev2D.th.nc: time- and space-varying along segment | elev2D.th.nc: combination of 3&4 | Must =0 | N/A | inu_elev
S&T, tracers | [MOD]_?.th: relax to time history (uniform along bnd) for inflow | Relax to constant for inflow | Relax to i.c. for inflow | [MOD]_3D.th.nc: relax to time- and space-varying values along bnd during inflow | N/A | N/A | N/A | inu_[MOD]
u,v | flux.th: via discharge (<0 for inflow!) | Constant discharge (<0 for inflow!) | Tidal velocity at each node (u,v components) | uv3D.th.nc: time- and space-varying along bnd (in lon/lat for ics=2) | uv3D.th.nc: combination of 3&4 | Flather (‘0’ for h) | Relax to uv3D.th.nc (2 separate relaxations for in & outflow) | inu_uv
bctides.in
Once you understand the b.c. flags, you can generate a draft bctides.in using pySCHISM (tides included): ….pyschism/examples/Bctides/gen_bctides.py

## Slide 35: .bp format
Your comments
24025
1 -90.4293 30.1689 0.30
2 -90.4313 30.1625 0.30
3 -90.4327 30.1559 0.20
4 -90.4320 30.1498 0.20
………………………………………
24025 -89.01 35.71 10.5
points
Used in many scripts
Basically a reduced .gr3 file without connectivity table
# of nodes or points

## Slide 36: Station.in
1 1 0 1 1 1 1 1 0 !on (1)|off(0) flags for elev, air pressure, windx, windy, T, S, u, v, w
4 !# of stations
1 6.5833 54.0000 0 !Format: station #,x,y,z; z is z-coordinate
2 7.1583 55.195 -1. !Fino3
3 6.35 54.1667 -5. !Ems
4 8.4514 54.7942 0 !PHoern
x,y must be consistent with hgrid.gr3 (projection or lon/lat)
Outputs are outputs/staout_[1-9]
z is z-coordinates, not distance from surface! So z<0 is below the datum
(build point format)

## Slide 37: *.th: ASCII
Corresponds to b.c. flag=1
Time (sec)
value 1 (1st bnd)
value 2 (2nd bnd)
value N (Nth bnd)
…………..
0. -0.084950529 0. -0.283168435 -0.226534754 -3.19980335 -16.367136
86400 -0.084950529 0. -0.283168435 -0.226534754 -3.19980335 -16.367136
172800 -0.084950529 0. -0.283168435 -0.226534754 -0.906139016 -22.2853565
259200 -0.084950529 0. -0.25485158 -0.226534754 -0.764554799 -16.367136
345600 -0.084950529 0. -0.25485158 -0.226534754 -0.764554799 -16.367136
432000 -0.084950529 0. -0.25485158 -0.226534754 -0.877822161 -16.367136
518400 -0.084950529 0. -0.25485158 -0.226534754 -3.17148638 -16.367136
604800 -0.084950529 0. -0.25485158 -0.226534754 -0.906139016 -16.367136
………………………………………………………………………………………………………….
Records must start from 0 and cover the entire simulation period, with equal time intervals
Time step is specified on the 2nd line
  Time steps ≥ main time step in param.nml
  Exception: time step in wind.th must match wtiminc in param.nml
flux.th (negative flow values for inflow)
e.g.: flux.th, elev.th, wind.th,…

## Slide 38: Point sources/sinks
Used to inject volume and mass (tracer) into the domain at specified locations (prisms)
  Momentum-less injection
  E.g., rainfall, outfall, runoff etc
if_source=1: requires additional 3 inputs
  source_sink.in: list of elements for sources and sinks
  vsource.th (needed if there is ≥1 source): time history of volume rate (m3/s) at each source. Rate must be ≥0;
  vsink.th (needed if there is ≥1 sink): time history of volume rate (m3/s) at each sink. Rate must be ≤0;
  msource.th (needed if there is ≥1 source): time history of tracer concentration (consistent unit) at each source. -9999 can be used to inject ambient concentration (in the absence of such info)
if_source=-1: requires source.nc (basically all the info specified in the 3 files)
Remember to change the sign when switching from flow open bnd to source!
2 ! total # of elements with sources
100 !global element # for 1st source
105 !global element # for 2nd source
!blank line for more readability
3 ! total # of elements with sinks
99 !global element # for 1st sink
100
105
source_sink.in
vsource.th
vsink.th
0. 1.2 0.5
0. 0.3
...
0. -1. -2.3 0.
7200. 0. -3. -1.3
...
msource.th
0. 10. 11. 0. 0.
3600. 9. 10. 0. 0.
...
T
S

## Slide 39: SCHISM input types: glossary
*.gr3: grid-like files (node centered): only hgrid.gr3 has b.c. info at the end
hgrid.ll: lon/lat form of horizontal grid (.gr3 format)
*.th*: time history (b.c.); ASCII or nc
*.ic: initial condition for elev, tracers (ASCII; most of them actually of .gr3 format)
sflux/: atmos. forcings (netcdf CF1.0)
param.nml: parameters
*.in: vgrid.in (vertical grid); bctides.in (b.c.) [ASCII]
*.prop: element centered property (ASCII)
*.nc: hotstart; tracer nudging inputs; b.c. time history inputs (type ‘4’ or ‘5’)

## Slide 40: Post-processing and visualization
Visualization
  python: schismview
  visIT: the best & most comprehensive tool for visualizing outputs; up to date and can viz shaved cells
  matlab: for in/outputs; not as efficient as VisIT
  GIS and google earth based: specialty tools; needs some customization
Extracting time series: vertical profiles, horizontal slabs, transects
  schismview or visIT
  station outputs (online): be careful not to abuse
  FORTRAN scripts: more flexible (‘offline’); read_output10* (for point, profile, transect)
    Linear interpolation in 3D (and time if necessary)
    Calculation of z-coordinates consistent with SCHISM code
    Beware wet/dry interpolation from elevation output
      Recall that elevations are defined at dry nodes
      Use wet/dry output flags as filter
      Best to exclude initial warm-up in analysis of compound flooding
Field averaging, harmonics analysis: FORTRAN scripts