## Slide 1: Lab: Delaware Bay 2D model

## Slide 2
Meshing procedure
In SMS
  Select disjoint nodes and delete them
On Sciclone: .2dm --> .gr3
Using gredit
  Check negative and skew elements
  Go back to SMS to fix meshing errors
  Check CFL>0.4 (need to convert lon/lat to map projection; e.g. using CPP; see last slide)
  Fix bad quads
  Pre-processing
  Load DEMs (reproject if needed)
Set up 2D runs

## Slide 3
Your tasks
Prepare and execute the pre-processor of SCHISM (refer to lecture notes on steps)
After the pre-proc step is successful, prepare inputs for 2D model
  gredit for .gr3 (manning.gr3, windrot_geo2proj.gr3)
  2 open segments: ocean and DE River
  Generate hgrid.ll (needed for nws=2): ln –sf hgrid.gr3 hgrid.ll
  Prepare param.nml, vgrid.in (60 days from July 1, 2018, GMT)
  PySCHISM: bctides.in (use tpxo), sflux (HRRR)
    TPXO or FES will need some databases in your dir ~/.local/share/. Do this:
    rsync –az ~yinglong/.local/share/ ~/.local/share/
  cd sflux; cp ~yinglong/DISKS/schism10/schism_verification_tests.2/Test_CORIE/sflux/sflux_*.txt .
  DE River flow from USGS at (from July 1, 2018): copy and rename it as flux.th cp /sciclone/home/yinglong/DISKS/vims20/MSCI602/RUN01b/Trenton_flow.DATA flux.th
Do a short run for DEB2D
  Simulation period from July 1, 2018 (30 - 60 days; time origin in GMT)
  Sciclone: use kuro or femto
  Play with inputs if you have time (e.g., SLR)
Post-proc and viz
  visit, schismview

## Slide 4
Mid-term project
Continue the DEB 2D model
Add 5 inch/day rainfall from Day 1 to 5, using script: /sciclone/home/yinglong/DISKS/vims20/MSCI602/RUN01b/edit_source
  But first, need to project from lon/lat to any map projection (CPP, UTM)
  Use this script for CPP projection (use a location inside mesh as center): /sciclone/home/yinglong/bin/cpp
  Rename the output as hgrid.gr3.proj and then run edit_source
Set up elev.ic for compound flood study (cf. lecture notes); edit param.nml
Run the model for 60 days
Study routing in watershed: what factors are important? (e.g., friction)
Submit your work:
  Your run dir with outputs
  Plots showing the maximum elevation (use ~yinglong/bin/combine_gr3)